MC CABLE CUTTER & PIGTAILER

Length of Whip Counter Kit Installation Instructions

(05/01/04)

Disclaimer: The cable length counter used, the Olympic Model 1410, is not specifically designed or recommended by the manufacturer for “BX” cable.  Initial tests out in the field by many MC Cable Cutter & Pigtailer users have shown that it works fine for MC cable as long as a smooth, consistent pulling motion is used.  With this in mind, we cannot guaranty the accuracy or durability of the counter when used for MC, HCF, or AC (as well as BX) cables.  Our liability is limited to the counter brackets/adapters and not the counter itself.  The counter and kit are also not available for the “Free” 30-day Trial.

Tools you might need will be: ¼” straight slot screwdriver, phillips-head screwdriver, 7/16” wrench or ratchet/socket, measuring tape or rule, hammer, center punch, 1/8” drill bit for pilot holes, 17/64” drill bit for mounting holes, drill motor, ¼-20 tap and tap holder.

In addition to these instructions, be sure to refer to the ones supplied by Olympic.  The counter can be mounted on either the right or left side of the machine.  It can also be used to measure other types of cable while attached to the machine.  Because of slight variations of MC Cable Cutter & Pigtailers over the years, earlier versions will have “extra” holes in them.  As reports come back from users, the unused holes will be eliminated to ease production.  Although the machine can be stored with the counter attached, this is not recommended as the counter or machine can be damaged.

The first step is to drill extra mounting holes in the rear mounting “legs” if they are not there already.  The holes should be 3” inboard and along the same line as the existing holes.  It will be easier to measure and drill these holes from below the machine.  Careful measurement will assure the holes you drill line up with the holes in the rear riser block and machine-side mounting bracket.  New machines will now be pre-drilled for optional counter attachment.

The next step is to determine where you want to mount the machine and counter.  The counter adds about a foot to the overall length of the machine.  Attach the riser blocks with the hardware provided and attach the machine-side bracket on the side you plan on putting the counter.  There are pre-tapped holes in the most common setting or you can tap your own in a different location, if necessary.  Clamp the machine to a work table/cart or you can use #10 screws through the mounting holes instead.

The counter-side bracket is attached to the machine-side bracket with hex-head screws to aid assembly/disassembly with a wrench when storing/setting-up (a screwdriver wouldn’t fit).  There are pre-tapped holes in the most common setting or you can tap your own in a different location, if necessary.  The holes are pre-drilled #7 for a ¼-20 tap.  Leave the screws loose for the next step.  The pre-tapped holes will align the counter 24” from the cut-off saw.

Attach the counter to the counter-side bracket with the included clevis pins and hairpins--two hairpins per clevis pin can be used.  The pins ease assembly/disassembly.  For more solid mounting you can use the screws/star-washer-nuts which came with the counter.  A 12” ½” drive socket extension or similar rigid item (½” diameter) is inserted into the counter and into the wear cone for alignment purposes.  Adjust the counter-side bracket so it is square to the machine-side bracket and the socket extension/rod is aligned straight into the wear cone.  Tighten the hex screws.  If the counter needs to be raised for proper alignment, use the provided 1/8” shim.  Attach the counter-side bracket to the work table with screws using the mounting holes down the center, if desired or necessary.  The counter is now ready for use.

To measure a whip, draw the cable from the reel/spool holder (recommended/required) through the counter, through the wear cone (if used) and up to the slot in the V-block.  Reset the counter.  Pull the cable smoothly and steadily to the desired length, then cut and pigtail with the MC Cable Cutter & Pigtailer.  Reset the counter and repeat.  Alternately, if you are cutting identical sizes of whips, instead of resetting the counter each time you can measure off multiples of the size desired (ie: 12’, 24’, 36’…etc.).  It would be good practice to initially and occasionally check the length measured against the actual length to determine the accuracy of the measurer and adjust for it if necessary.

Please feel free to call (407) 474-6400 if you have any additional questions…

McCutter, Inc., 1930 N. Kingway Dr., Deltona, FL  32738

Visit Our Website: www.mccutter.com